Advanced Computer Architecture
03 February 2015

A) A processor embeds four cores that have private L1 caches; two L2 caches are shared by each couple of cores; the single L3 cache is shared by the four cores. The caches obey the MESI protocol and have the following structure: 32KB, 2-way L1 I-cache and D-cache, each 16-byte block; 512 KB, 4-way associative, 32-byte block L2 cache; 4MB, 4-way associative, 64-byte block shared L3 cache. The latencies (disregarding virtual memory TLB) expressed in clock cycles are: 3 in L1, 6 in L2, 10 in L3. Addresses are 48-bit long. Assuming initially empty and invalidated cache lines throughout the hierarchy, consider the following memory access

core 1) LD F1, 0000FFFFA000hex;

- a) show the block involved in each cache, and the associated MESI state;

- b) show a memory access instruction (that uses an address different from 0000FFFFA000hex ) that places the L1 block of L1 cache of core 1 in state S, and specify the cache block state for all other cache blocks involved;

- c) show a memory access instruction that places the L1 block of L1 cache of core 1 in state I, and specify the cache block state for all other cache blocks involved (consider the situation of the caches as produced from the operation of point b).

B) The processor runs at 2.6GHz, and has two 64-bit external busses, each driven by a memory interface module capable of sustaining 1.8 GT/sec.
The external RAM is realized with DDR3 chips and is logically organized with 2 banks, each capable of delivering a 16-bit word. Addressing the memory subsystems requires two bus cycles, and activating a memory row requires 2 bus clock cycles. Using the attached table, choose a DDR3 module that allows to sustain a burst transfer mode from DDRAM compatible with the memory interface of the processor and estimate the cost of a miss for the above described cache hierarchy, assuming that a memory reference does not span across busses (a mem request is forwarded to a single bus).

C) Each core of the processor is organized as a superscalar, 2-way pipeline, that fetches, decodes issues and retires (commits) bundles containing each 2 instructions. The front-end in-order section (fetch and decode) consists of 2 stages. The issue logic takes 1 clock cycle, if the instructions in the bundle are independent, otherwise it takes 2 clock cycles. The architecture supports dynamic speculative execution, and control dependencies from branches are solved when the branch evaluates the condition, even if it is not at commit. The execution model obeys the attached state transition diagram. There is a functional units (FUs) Int1 for integer arithmetics (arithmetic and local instructions, branches and jumps, no multiplication, 2 FUS FAdd1-Fadd2 for floating point addition/subtraction, a FU FMolt1 for floating point multiplication, and a FU for division, FDiv1.

There are 12 integer (R0-R11) and 12 floating point (F0-F11) registers. Speculation is handled through a 8-entry ROB, a pool of 4 Reservation Stations (RS) Rs1-4 shared among all FUs, 2 load buffers Load1 and Load2, 1 store buffer Store1 (see the attached execution model): an instruction bundle is first placed in the ROB (if two entries are available), then up to 2 instructions are dispatched to the shared RS (if available) when they are ready for execution and then executed in the proper FU. FUs are pipelined (not the Fdiv one) and have the latencies quoted in the following table:

| Int - 2 | Fadd – 4 |
| --- | --- |
| Fmolt – 6 | Fdiv – 10 |

- The code is assumed to be already in the I-cache; data caches are described in point A) and are assumed empty and invalidated; the cost of a miss is conventionally set to 50 processor clock cycles, irrespective of what has been computed at point B.

c1) assuming a write-through protocol for cache management, show state transitions for the instructions of the first iteration of the following code fragment, that scans the 1024 floating elements, each 8-byte, of array X[] and Y[] and replaces X[i] with Y[i] and Y[i] with Y[i]+X[i+1] (R0 is always 0).

PC01 OR    R1,R0,00000FFFFA000hex -- set base address of X[0]

PC02 OR    R2,R0,00000FFFF0000hex -- set base address of Y[0]

PC03 OR    R5,R0,1024dec          –- set loop terminating condition

PC04 OR    R3,R0,R0              -- initialize loop controlling variable

PC05 LD    F0,0(R1)              -- load X[i]

PC06 LD    F1,0(R2)              -- load Y[i]

PC07 ST    F1,0(R1)              -- store Y[i] into X[i]

PC08 ADDF  F3,F1,F0

PC09 ADD   R1,R1,8               -- advance pointer into array X

PC10 ST    F3,0(R2)              -- store X[i]+Y[i] into Y[i]

PC11 ADD   R3,R2,1               -- increase loop controlling variable

PC12 ADD   R2,R1,8               -- advance pointer into array Y

PC13 BLE   R5,R3,PC05            -- testing for loop exit condition

c2) show ROB, RS and buffer status at the issue of PC05 in the second iteration;

c3) determine the number of hits and misses in each cache level for the algorithm;

c4) answer each of the following question:

- would the number of misses (all levels) change, if the dimension of the L1 D cache were doubled (from 32KB to 64 KB) ?

- does the execution of the algorithm causes a block replacement in any cache level ?

- would it be better to decrease the latency of L1 to 1 clock cycle, or doubling the troughput of the memory bus ?

Dynamic speculative execution

Decoupled ROB RS execution model

| ISTRUCTION |  |  | INSTRUCTION STATE |
| --- | --- | --- | --- |
|  | n. ite | ROB pos | WO | RE | DI | EX | WB | RR | CO |
| PC01 OR R1,R0,00000FFFFA000hex |  |  |  |  |  |  |  |  |  |
| PC02 OR R2,R0,00000FFFF0000hex |  |  |  |  |  |  |  |  |  |
| PC03 OR R5,R0,1024dec |  |  |  |  |  |  |  |  |  |
| PC04 OR R3,R0,R0 |  |  |  |  |  |  |  |  |  |
| PC05 LD F0,0(R1) |  |  |  |  |  |  |  |  |  |
| PC06 LD F1,0(R2) |  |  |  |  |  |  |  |  |  |
| PC07 ST F1,0(R1) |  |  |  |  |  |  |  |  |  |
| PC08 ADDF F3,F1,F0 |  |  |  |  |  |  |  |  |  |
| PC09 ADD R1,R1,8 |  |  |  |  |  |  |  |  |  |
| PC10 ST F3,0(R2) |  |  |  |  |  |  |  |  |  |
| PC11 ADD R3,R3,1 |  |  |  |  |  |  |  |  |  |
| PC12 ADD R2,R2,8 |  |  |  |  |  |  |  |  |  |
| PC13 BLE R5,R3,PC05 |  |  |  |  |  |  |  |  |  |

|  | Reservation station and load/store buffers |
| --- | --- |
|  | Busy | Op | Vj | Vk | ROBj | ROBk | ROB pos | Address |
| Rs1 |  |  |  |  |  |  |  |  |
| Rs2 |  |  |  |  |  |  |  |  |
| Rs3 |  |  |  |  |  |  |  |  |
| Rs4 |  |  |  |  |  |  |  |  |
| Load1 |  |  |  |  |  |  |  |  |
| Load2 |  |  |  |  |  |  |  |  |
| Store1 |  |  |  |  |  |  |  |  |

ROBj ROBk: sources not yet available

ROB pos: ROB entry number where instruction is located

|  | Result Register status |
| --- | --- |
| Integer | R0 | R1 | R2 | R3 | R4 | R5 | R6 | R7 | R8 | R9 | R10 | R11 |  |  |
| ROB pos |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| state |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Float. | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 |  |  |
| ROB pos |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| state |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Reorder Buffer (ROB) |
| --- |
| ROB Entry# | Busy | Op | Status | Destination | Value |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |
| 5 |  |  |  |  |  |
| 6 |  |  |  |  |  |
| 7 |  |  |  |  |  |
| 8 |  |  |  |  |  |

Decoupled execution model for bundled (paired) instructions

The state diagram depicts the model for a dynamically scheduled, speculative execution microarchitecture equipped with a Reorder Buffer (ROB) and a set of Reservation Stations (RS). The RSs are allocated during the ISSUE phase, denoted as RAT (Register Alias Allocation Table) in INTEL microarchitectures, as follows: a bundle (2 instructions) if fetched from the QUEUE of decoded instructions and ISSUED if there is a free couple of consecutive entries in the ROB ( head and tail of the ROB queue do not match); a maximum of two instruction are moved into the RS (if available) when all of their operands are available. Access memory instructions are allocated in the ROB and then moved to a load/store buffer (if available) when operands (address and data, if proper) are available .

States are labelled as follows:

WO:	Waiting for Operands (at least one of the operands is not available)

RE:	Ready for Execution (all operands are available)

DI:	Dispatched (posted to a free RS or load/store buffer)

EX:	Execution (moved to a load/store buffer or to a matching and free UF)

WB:	Write Back (result is ready and is returned to the Rob by using in exclusive mode the Common Data Bus CDB)

RR:	Ready to Retire (result available or STORE has completed)

CO:	Commit (result is copied to the final ISA register)

State transitions happen at the following events:

from QUEUE to WO:	ROB entry available, operand missing

from QUEUE to RE:	ROB entry available, all operands available

loop at WO:	waiting for operand(s)

from WO to RE:	all operands available

loop at RE:	waiting for a free RS or load/store buffer

from RE to DI:	RS or load/store buffer available

loop on DI:	waiting for a free UF

from DI to EX:	UF available

loop at EX:	multi-cycle execution in a UF, or waiting for CDB

from EX to WB:	result written to the ROB with exclusive use of CDB

from EX to RR:	STORE completed, branch evaluted

loop at RR:	instruction completed, not at the head of the ROB, or bundled with a not RR instruction

from RR to CO:	bundle of RR instructions at the head of the ROB, no exception raised

Resources
Register-to-Register instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

RS: state DI

UF: EX and WB

Load/Store instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

Load buffer: from state WO (or RE) up to WB

Store buffer: from state WO (or RE) up to EX (do not use WB)

Forwarding: a write on the CDB (WB) makes the operand available to the consumer in the same clock cycle. If the consumer is doing a state transition from QUEUE to WO or RE, that operand is made available; if the consumer is in WO, it goes to RE in the same clock cycle of WB for the producer.

Branches: they compute Next-PC and the branch condition in EX and optionally forward Next-PC to the “in-order” section of the pipeline (Fetch states) in the next clock cycle. They do not enter WB and go to RR instead.

| Standard name | Memory clock (MHz) | Cycle time (ns) | I/O bus clock (MHz) | Data rate (MT/s) | Module name | Peak transfer rate (MB/s) |
| --- | --- | --- | --- | --- | --- | --- |
| DDR3-800D DDR3-800E | 100 | 10 | 400 | 800 | PC3-6400 | 6400 |
| DDR3-1066E DDR3-1066F DDR3-1066G | 133⅓ | 7 1⁄2 | 533⅓ | 1066⅔ | PC3-8500 | 8533⅓ |
| DDR3-1333F* DDR3-1333G DDR3-1333H DDR3-1333J* | 166⅔ | 6 | 666⅔ | 1333⅓ | PC3-10600 | 10666⅔ |
| DDR3-1600G* DDR3-1600H DDR3-1600J DDR3-1600K | 200 | 5 | 800 | 1600 | PC3-12800 | 12800 |
| DDR3-1866J* DDR3-1866K DDR3-1866L DDR3-1866M* | 233⅓ | 4 2⁄7 | 933⅓ | 1866⅔ | PC3-14900 | 14933⅓ |
| DDR3-2133K* DDR3-2133L DDR3-2133M DDR3-2133N* | 266⅔ | 3 3⁄4 | 1066⅔ | 2133⅓ | PC3-17000 | 17066⅔ |

DDR3 standard JEDEC specification (source Wikipedia)

# Text boxes

wo

DI

EX

WB

RR

RE

CO

QUEUE