Advanced Computer Architecture
26 Giugno 2014

A) A processor has the following cache hierarchy: 16KB, 2-way L1 I-cache, 16 KB 4-way L1 D-cache, each 16-byte block; 512 KB, 4-way associative, 32-byte block L2 cache; 4MB, 8-way associative, 64-byte block L3 cache. L1 and L2 cache apply write-through policy, while L3 uses write back. The latencies (disregarding virtual memory TLB) expressed in clock cycles are: 4 in L1, 10 in L2, 25 in L3. Addressing uses 48 bits. Caches use a write no-allocate policy.

a1) L3 is built using 1x4Mb SRAM chips. Compute the number of chips necessary.

a2) Assuming initially empty and invalidated cache lines throughout the hierarchy, show the content of each D-cache after the execution of the instruction ST F1,(0000000AAFA1hex) (further assumption: the instruction is already in the I-cache).

B) Consider the following pseudo-code fragment acting on the elements of an array X[.] of 1024 8-byte floating point entries:

for (i=0;i<1023;i=i+2)

Y=X[i+1]

X[i+1]=X[i]

X[i]=Y

b1) assuming empty and invalidated D-caches, compute the number of misses in all levels of the cache hierarchy.

b2) discuss if the loop can be unrolled.

b1)

The array elements are 8-byte long. The caches have blocks size of 16(L1), 32(L2), 64(L3). If the compiler does a good job in allocating the array (with x[0] aligned to 64-by boundary), the elements will be contained in cache blocks as follows (- L1; + L2; #L3)

X[0]X[1]-X[2]X[3]-X[4]X[5]|-X[6]X[7]

-------- -------- -------- ---------

+++++++++++++++++ ++++++++++++++++++

####################################

Access to X[i+1] loads a block containing X[i] as well. So, the above loop contains two reads, and two writes. The first read can miss, the subsequent read and the two write always hit.

The pattern is

X[0]X[1]-X[2]X[3]-X[4]X[5]|-X[6]X[7]

iter.    1      2       3     4

read  Miss L3 hit L2 hit L3 hit L2

read  hit  L1 hit L1 hit L1 hit L1

write hit  L1 hit L1 Hit L1 hit L1

write hit  L1 Hit L1 Hit L1 Hit L1

SO there will 512/4=128 miss L3; 512/2=256 miss L2; 512/1 miss L1

b2) discuss if the loop can be unrolled.

Iteration (i+2) does not use the output of iteration (i), each iteration is independent of any other.

iter. (i)          iter (i+2)

Y=X[i+1]           Y=X[i+3]

X[i+1]=X[i]        X[i+3]=X[i+2]

X[i]=Y             X[i+2]=Y

The loop can be unrolled, obviously the amount of unrolling will be limited by hardware resources (registers) available.

C) The processor has a superscalar, 2-way pipeline, that fetches, decodes issues and retires (commits) bundles containing each 2 instructions. The front-end in-order section (fetch and decode) consists of 2 stages. The issue logic takes 1 clock cycle, if the instructions in the bundle are independent, otherwise it takes 2 clock cycles. The architecture supports dynamic speculative execution, and control dependencies from branches are solved when the branch evaluates the condition, even if it is not at commit. The execution model obeys the attached state transition diagram.

There are 2 functional units (FUs) Int1-INT2 for integer arithmetics (arithmetic and local instructions, branches and jumps, no multiplication ), 2 FUS FAdd1-Fadd2 for floating point addition/subtraction, a FU FMolt1 for floating point multiplication, and a FU for division, FDiv1.

There are 12 integer (R0-R11) and 12 floating point (F0-F11) registers.

Speculation is handled through a 8-entry ROB, a pool of 4 Reservation Stations (RS) Rs1-4 shared among all FUs, 2 load buffers Load1-2, 2 store buffers Store1-2 (see the attached execution model): an instruction bundle is first placed in the ROB (if two entries are available), then each instruction is dispatched to one of the shared RS (if available) and then executed in the proper FU. FUs are pipelined (not the Fdiv one) and have the latencies quoted in the following table:

| Int - 2 | Fadd – 3 |
| --- | --- |
| Fmolt – 5 | Fdiv – 6 |

Further assumption

- Data caches are described in point A) and are assumed empty and invalidated.

c1) show state transitions for the instructions of the first two iterations of the following code fragment (assume a conventional miss time of 60 clock cycles), highlighting conflicts, if any:

PC01 MOVI  R1, 0000000AAFA1hex – set base address of X[0]

PC02 MOVI  R5, 1023          – set loop terminating condition

PC03 MOVI  R2, 0             -- initialize loop controlling variable

PC04 LD    F4,8(R1)         -- load X[i+1]

PC05 LD    F5,0(R1)          -- load X[i]

PC06 ST    F5,8(R1)         -- store into X[i+1]

PC07 ST    F4,0(R1)          -- store into X[i]

PC08 ADD   R2,R2,2           -- increase loop controlling variable

PC09 ADD   R1,R1,16          -- advance pointer into array by 2

PC10 BL    R5,R2,PC04        -- testing for loop exit condition

c2) show ROB, RS and buffer status at the issue of the BL of the first iteration;

c3) estimate the CPI of the algorithm;

Dynamic speculative execution

Decoupled ROB RS execution model

| ISTRUCTION |  |  | INSTRUCTION STATE |
| --- | --- | --- | --- |
|  | n. ite | ROB pos | WO | RE | DI | EX | WB | RR | CO |
| PC01 MOVI R1, 0000000AAFA1 | 1 | 1 |  | 1 | 2 | 3-4 | 5 | 6-7 | 8 |
| PC02 MOVI R5, 1023 | 1 | 2 |  | 1-2 | 3 | 4-5 | 6 | 7 | 8 |
| PC03 MOVI R2, 0 | 1 | 3 |  | 2-3 | 4 | 5-6 | 7 | 8-107 | 108 |
| PC04 LD F4,8(R1) | 1 | 4 | 2-4 | 5 | 6 | 7-105 | 106 | 107 | 108 |
| PC05 LD F5,0(R1) | 1 | 5 | 3-4 | 5-6 | 7 | 8-106 | 107 | 108-148 | 149 |
| PC06 ST F5,8(R1) | 1 | 6 | 4-106 | 107 | 108 | 109-147 | - | 148 | 149 |
| PC07 ST F4,0(R1) | 1 | 7 | 5-105 | 106 | 107 | 108-146 | - | 147-149 | 150 |
| PC08 ADD R2,R2,2 | 1 | 8 | 5-6 | 7 | 8 | 9-10 | 11 | 12-149 | 150 |
| PC09 ADD R1,R1,16 | 1 | 1 |  | 9 | 10 | 11-12 | 13 | 15-150 | 151 |
| PC10 BL R5,R2,PC04 | 1 | 2 | 9-10 | 11 | 12 | 13-14 | - | 15-150 | 151 |
| PC04 LD F4,8(R1) | 2 | 3 |  | 109 | 110 | 111-124 | 125 | 126-151 | 152 |
| PC05 LD F5,0(R1) | 2 | 4 |  | 109-110 | 111 | 112-125 | 126 | 127-151 | 152 |
| PC06 ST F5,8(R1) | 2 | 5 |  | 150 | 151 | 152-190 | - | 191-192 | 193 |
| PC07 ST F4,0(R1) | 2 | 6 |  | 150-151 | 152 | 153-191 | - | 192 | 193 |
| PC08 ADD R2,R2,2 | 2 | 7 |  | 151-152 | 153 | 154-155 | 156 | 157-193 | 194 |
| PC09 ADD R1,R1,16 | 2 | 8 |  | 151-153 | 154 | 155-156 | 157 | 158-193 | 194 |
| PC10 BL R5,R2,PC04 | 2 | 1 | 152-155 | 156 | 157 | 158-159 | - | 160-194 | 195 |
| PC11 ISTR A (CANCELLED at 160) | - | 2 |  |  |  |  |  |  |  |

Cache models and latencies:

Miss: 4+10+25+60= 99 (clock cycle)

LD hit L1: 4

LD hit L2: 4+10=14

LD hit L3: 4+10+25=39

Write policy: write-through (wt) L1, L2; write-back (wb) L3 (write no-allocate)

ST hit L1: 4+10+25=39 because of wt

ST hit L2: 4+10+25=39 because of wt

ST hit L3: 4+10+25=39 if no block replacement because of wb

4+10+25+60=99 if block replacement

ST miss L1 hit L2 = 4+10+25=39 because of wt

ST miss L2 hit L3 = 4+10+25=39

ST miss L3 = Miss = 4+10+25+60=99

Conflicts

data: RAW

structural: ISSUE (bundle), DI (reservation station), ROB (slots)

Cache: miss, hit-on-miss, hit wt, hit L2

c3) Estimate of the CPI of the algorithm

Number of iteration = 1024/2= 512

Number of instructions in the preamble to the loop = 3

Number of instrcution in the loop body = 7

IPL (number of instructions executed): 3 + 7 * 512 = 3587

Clock cycle for the whole algorithm: itr would be necessary to complete 4 cycles of the loop, since every four cycle there is a miss, which costs 99 clock cycle. The lateny of this miss is exposed only partially. Indeed the first iteration takes 151 clocl cycle, the second 45 more clock cycles, and it is likely that the third (miss L2 hit L3) adds some 25 clocks to the 45 required by the previous. So one can expect the following pattern evry four iterations:

iter 1 = 150

iter 2 =  45

iter 3 =  70

iter 4 =  45

Grand total for 4 iterations= 310

The fetch and decode time (two pipeline stages) are hidden by the stalls induced by the ROB full condition. In any case, their contribution to the execution time would be minimal since we assume that the code is in the I-cache.

Total clock cycle = 310 * 512 / 4 = 39680

Estimated CPI = Total clock cycle / IPL = 39680 /3587 = 11,06

|  | Reservation station and load/store buffers at clock 9 |
| --- | --- |
|  | Busy | Op | Vj | Vk | ROBj | ROBk | ROB pos | Address |
| Rs1 |  |  |  |  |  |  |  |  |
| Rs2 |  |  |  |  |  |  |  |  |
| Rs3 |  |  |  |  |  |  |  |  |
| Rs4 |  |  |  |  |  |  |  |  |
| Load1 | y | LD F4,8(R1) |  |  |  |  | 4 | [R1]+8 |
| Load2 | y | LD F5,0(R1) |  |  |  |  | 5 | [R1] |
| Store1 |  |  |  |  |  |  |  |  |
| Store2 |  |  |  |  |  |  |  |  |

ROBj ROBk: sources not yet available

ROB pos: ROB entry number where instruction is located

|  | Result Register status |
| --- | --- |
| Integer | R0 | R1 | R2 | R3 | R4 | R5 | R6 | R7 | R8 | R9 | R10 | R11 |  |  |
| ROB pos |  | 1 | 3 |  |  |  |  |  |  |  |  |  |  |  |
| state |  | P | p |  |  |  |  |  |  |  |  |  |  |  |
| Float. | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 |  |  |
| ROB pos |  |  |  |  | 4 | 5 |  |  |  |  |  |  |  |  |
| state |  |  |  |  | P | P |  |  |  |  |  |  |  |  |

| Reorder Buffer (ROB) |
| --- |
| ROB Entry# | Busy | Op | Status | Destination | Value |
| 1 | y | PC09 | RE | R1 | [R1]+16 |
| 2 | y | PC10 | WO |  | PC04 |
| 3 | y | PC03 | RR | R2 | 0 |
| 4 | y | PC04 | EX | F4 | [mem([R1]+8)] |
| 5 | y | PC05 | EX | F5 | mem([R1]) |
| 6 | y | PC06 | WO | mem([R1]+8) | ROB(5) |
| 7 | y | PC07 | WO | mem([R1]) | ROB(4) |
| 8 | y | PC08 | EX | R2 | [R2]+2 |

D) The processor runs at 2GHz, and the external bus allows a burst transfer rate of 12GB/sec. Measure the effective gain for the code fragment as a consequence of the following architectural improvements:

d1) CPU boost on integer arithmetic instruction: boosted clock 2.5 GHz;

d2) L3 latency reduced to 15 clock cycles;

d3) external bus transfer rate increased to 16GB/sec.

Decoupled execution model for bundled (paired) instructions

The state diagram depicts the model for a dynamically scheduled, speculative execution microarchitecture equipped with a Reorder Buffer (ROB) and a set of Reservation Stations (RS). The RSs are allocated during the ISSUE phase, denoted as RAT (Register Alias Allocation Table) in INTEL microarchitectures, as follows: a bundle (2 instructions) if fetched from the QUEUE of decoded instructions and ISSUED if there is a free couple of consecutive entries in the ROB ( head and tail of the ROB queue do not match); each single instruction is moved into a RS (if available) when all of its operands are available. Access memory instructions are allocated in the ROB and then moved to a load/store buffer (if available) when operands (address and data, if proper) are available .

States are labelled as follows:

WO:	Waiting for Operands (at least one of the operands is not available)

RE:	Ready for Execution (all operands are available)

DI:	Dispatched (posted to a free RS or load/store buffer)

EX:	Execution (moved to a load/store buffer or to a matching and free UF)

WB:	Write Back (result is ready and is returned to the Rob by using in exclusive mode the Common Data Bus CDB)

RR:	Ready to Retire (result available or STORE has completed)

CO:	Commit (result is copied to the final ISA register)

State transitions happen at the following events:

from QUEUE to WO:	ROB entry available, operand missing

from QUEUE to RE:	ROB entry available, all operands available

loop at WO:	waiting for operand(s)

from WO to RE:	all operands available

loop at RE:	waiting for a free RS or load/store buffer

from RE to DI:	RS or load/store buffer available

loop on DI:	waiting for a free UF

from DI to EX:	UF available

loop at EX:	multi-cycle execution in a UF, or waiting for CDB

from EX to WB:	result written to the ROB with exclusive use of CDB

from EX to RR:	STORE completed, branch evaluted

loop at RR:	instruction completed, not at the head of the ROB, or bundled with a not RR instruction

from RR to CO:	bundle of RR instructions at the head of the ROB, no exception raised

Resources
Register-to-Register instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

RS: state DI

UF: EX and WB

Load/Store instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

Load buffer: from state WO (or RE) up to WB

Store buffer: from state WO (or RE) up to EX (do not use WB)

Forwarding: a write on the CDB (WB) makes the operand available to the consumer in the same clock cycle. If the consumer is doing a state transition from QUEUE to WO or RE, that operand is made available; if the consumer is in WO, it goes to RE in the same clock cycle of WB for the producer.

Branches: they compute Next-PC and the branch condition in EX and optionally forward Next-PC to the “in-order” section of the pipeline (Fetch states) in the next clock cycle. They do not enter WB and go to RR instead.

# Text boxes

wo

DI

EX

WB

RR

RE

CO

QUEUE