Advanced Computer Architecture
November 2014

A) A processor embeds four cores that have private L1 caches; two L2 caches are shared by each couple of cores; the single L3 cache is shared by the four cores. The caches obey the MESI protocol and have the following structure: 32KB, 2-way L1 I-cache and D-cache, each 16-byte block; 1 MB, 4-way associative, 32-byte block L2 cache; 8MB, 8-way associative, 128-byte block shared L3 cache. The latencies (disregarding virtual memory TLB) expressed in clock cycles are: 4 in L1, 8 in L2, 24 in L3. Addresses are 48-bit long.

a1) assuming initially empty and invalidated cache lines throughout the hierarchy, consider the following memory accesses

core 1) LD F1, 0000FFFFA000hex;

core 2) LD F1, 0000FFFFA010hex;

core 3) LD F1, 0000FFFFA010hex

core 4) ST F1, 0000FFFFA020 hex;

and show the cache blocks involved throughout the memory hierarchy and the sequence of miss/hit in the hierarchy (assume writes are managed with a write-back policy).

a2) show the status of each cache block according to the MESI protocol at each operation.

Assumptions: L2 caches are shared by cores 1-2, and 3-4; we arbitrary assume that MESI is applied both at L1/L2 and L2/L3 interfaces.

L1(I&D): NB=32KB/16B=2K; 2-way; index=log2(2K/2)=10 bits; block disp=4 bits; tag=48-10-4=34 bits

L2: NB=1MB/32B=2^15; 4-way; index=log2(2^15/4)=13 bits; block disp=5 bits; tag=48-13-5=30 bits

L3: NB=8MB/128B=2^16; 8-way; index=log2(2^16/8)=13 bits; block disp=7 bits; tag=48-13-7=28 bits

CORE 1) LD F1, 0000FFFFA000hex

miss L3, L2, L1

0000|0000|0000|0000|1111|1111|1111|1111|1010|0000|0000|0000

L3

0000000000000000111111111111|1111101000000|0000000 ; way 1;

L2(1-2)

000000000000000011111111111111|1110100000000|00000 ; way 1; block status E

L1(1)

0000000000000000111111111111111110|1000000000|0000 ; way 1; block status E

CORE 2) LD F1, 0000FFFFA010hex

miss L1, hit L2

0000|0000|0000|0000|1111|1111|1111|1111|1010|0000|0001|0000

L3

0000000000000000111111111111|1111101000000|0010000 ; way 1;

L2(1-2)

000000000000000011111111111111|1110100000000|10000 ; way 1; block status S

L1(2)

0000000000000000111111111111111110|1000000001|0000 ; way 1; block status E

CORE 3) LD F1, 0000FFFFA010hex

miss L1, miss L2, hit L3

0000|0000|0000|0000|1111|1111|1111|1111|1010|0000|0001|0000

L3

0000000000000000111111111111|1111101000000|0010000 ; way 1;

L2(3-4)

000000000000000011111111111111|1110100000000|10000 ; way 1; block status S

L1(3)

0000000000000000111111111111111110|1000000001|0000 ; way 1; block status S

L1(2)

0000000000000000111111111111111110|1000000001|0000 ; way 1; block status S

CORE 4) ST F1, 0000FFFFA020hex

miss L1, miss L2, hit L3

0000|0000|0000|0000|1111|1111|1111|1111|1010|0000|0010|0000

L3

0000000000000000111111111111|1111101000000|0100000 ; way 1; dirty

L2(3-4)

000000000000000011111111111111|1110100000001|00000 ; way 1; block status I

L1(4)

0000000000000000111111111111111110|1000000010|0000 ; way 1; block status M

due to write back, L2(3-4) is not updated

B) The processor runs at 2.6GHz, and the 64-bit external bus allows a maximum transfer rate of 12 GB/sec.
The external RAM is realized with DDR3-2133 chips and is logically organized with 4 banks, each capable of delivering a 16-bit word. Addressing the memory subsystems requires two bus cycles, and activating a memory row requires 3 bus clock cycles. Assuming burst transfer mode from DDRAM, estimate the cost of a miss.

Bus maximum transfer rate is 12GB/sec: bus width is 8 bytes, the maximum transfer rate allows for  12/8 Gtransfer/sec, that is a 12/8/2 GHz clock, 750MHz clock (with DDR mode, that is 2 trasfers per clock cycle). Since DDR3-2133 runs at maximum clock of 1066 MHz, the bus is the limiting factor.

The miss requires the transfer of a L3 cache block, that is 128 bytes.

Tmiss= Tind+Natt*Tatt+Nt*0,5 (T in bus clock cycles)

Tmiss=2+(128/(4*2))* 3+(128/8)*0,5=2+16*3+16*0,5=58 (bus clock cycles)

The number of processor clock cycles is 58 *  2.6 10^9 /750 10^6 =58*2.6/0,75=201,06; that is 202.

Total miss cost including all latencies is 4+8+24+202=238 processor clock cycles

C) Each core of the processor is organized as a superscalar, 2-way pipeline, that fetches, decodes issues and retires (commits) bundles containing each 2 instructions. The front-end in-order section (fetch and decode) consists of 2 stages. The issue logic takes 1 clock cycle, if the instructions in the bundle are independent, otherwise it takes 2 clock cycles. The architecture supports dynamic speculative execution, and control dependencies from branches are solved when the branch evaluates the condition, even if it is not at commit. The execution model obeys the attached state transition diagram. There is a functional units (FUs) Int1 for integer arithmetics (arithmetic and local instructions, branches and jumps, no multiplication, 2 FUS FAdd1-Fadd2 for floating point addition/subtraction, a FU FMolt1 for floating point multiplication, and a FU for division, FDiv1.

There are 12 integer (R0-R11) and 12 floating point (F0-F11) registers. Speculation is handled through a 8-entry ROB, a pool of 4 Reservation Stations (RS) Rs1-4 shared among all FUs, 1 load buffers Load1, 1 store buffer Store1 (see the attached execution model): an instruction bundle is first placed in the ROB (if two entries are available), then up to 2 instructions are dispatched to the shared RS (if available) when they are ready for execution and then executed in the proper FU. FUs are pipelined (not the Fdiv one) and have the latencies quoted in the following table:

| Int - 2 | Fadd – 3 |
| --- | --- |
| Fmolt – 5 | Fdiv – 6 |

Further assumption

- The code is assumed to be already in the I-cache; data caches are described in point A) and are assumed empty and invalidated; the cost of a miss is that computed at point B.

c1) assuming a write-back protocol for cache management, show state transitions for the instructions of the first iteration of the following code fragment, that scans the 1024 floating elements, each 8-byte, of array X[] and replaces X[i] with X[i]+X[i+1] (R0 is always 0).

PC01 OR    R1,R0,00000FFFFA000hex -- set base address of X[0]

PC02 OR    R5,R0,1023dec          –- set loop terminating condition

PC03 OR    R3,R0,R0              -- initialize loop controlling variable

PC04 LD    F0,0(R1)              -- load X[i]

PC05 LD    F1,8(R1)              -- load X[i+1]

PC06 ADDF  F2,F1,F0              -- new value for X[i]

PC07 ST    F2,0(R1)              -- written back

PC08 ADD   R3,R3,2               -- increase loop controlling variable

PC09 ADD   R1,R1,16              -- advance pointer into array X

PC10 BL    R5,R3,PC04            -- testing for loop exit condition

c2) show ROB, RS and buffer status at the issue of PC04 in the second iteration;

c3) determine the number of hits and misses in each cache level for the algorithm;

c4) estimate the CPI of the algorithm and the execution time;

c5) which is the speed-up that can be expected by halving the latency of L3?

Dynamic speculative execution

Decoupled ROB RS execution model

| ISTRUCTION |  |  | INSTRUCTION STATE |
| --- | --- | --- | --- |
|  | n. ite | ROB pos | WO | RE | DI | EX | WB | RR | CO |
| PC01 OR R1,R0,00000FFFFA000hex |  | 1 |  | 1 | 2 | 3-4 | 5 | 6-7 | 8 |
| PC02 OR R5,R0,1023dec |  | 2 |  | 1 | 2-3 | 4-5 | 6 | 7 | 8 |
| PC03 OR R3,R0,R0 |  | 3 |  | 2 | 3-4 | 5-6 | 7 | 8-246 | 247 |
| PC04 LD F0,0(R1) |  | 4 | 2-4 | 5 | 6 | 7-244 | 245 | 246 | 247 |
| PC05 LD F1,8(R1) |  | 5 | 3-4 | 5-245 | 246 | 247-250 | 251 | 252-257 | 258 |
| PC06 ADDF F2,F1,F0 |  | 6 | 4-250 | 251 | 252 | 253-255 | 256 | 257 | 258 |
| PC07 ST F2,0(R1) |  | 7 | 5-255 | 256 | 257 | 258-261 | - | 262 | 263 |
| PC08 ADD R3,R3,2 |  | 8 | 5-6 | 7 | 8 | 9-10 | 11 | 12-262 | 263 |
| PC09 ADD R1,R1,16 |  | 1 |  | 9 | 10 | 11-12 | 13 | 14-263 | 264 |
| PC10 BL R5,R3,PC04 |  | 2 | 9-10 | 11 | 12 | 13-14 | - | 15-263 | 264 |

PC10 decides on the branch at clock 14, so PC04 (together with PC05) is fetched at 15, decoded at 16; at 17 it cannot be issue, because the ROB is full until 247 included, so PC04 is issued together with PC05 at 248 and placed in ROB positions 3 and 4.

clock 248

|  | Reservation station and load/store buffers |
| --- | --- |
|  | Busy | Op | Vj | Vk | ROBj | ROBk | ROB pos | Address |
| Rs1 | no |  |  |  |  |  |  |  |
| Rs2 | no |  |  |  |  |  |  |  |
| Rs3 | no |  |  |  |  |  |  |  |
| Rs4 | no |  |  |  |  |  |  |  |
| Load1 | yes | PC05 |  |  |  |  | 5 | [8(R1)] |
| Store1 | no | PC07 |  |  |  |  | 7 | [(R1)] |

ROBj ROBk: sources not yet available

ROB pos: ROB entry number where instruction is located

|  | Result Register status |
| --- | --- |
| Integer | R0 | R1 | R2 | R3 | R4 | R5 | R6 | R7 | R8 | R9 | R10 | R11 |  |  |
| ROB pos |  | 1 |  | 8 |  |  |  |  |  |  |  |  |  |  |
| state |  | B |  | B |  |  |  |  |  |  |  |  |  |  |
| Float. | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 |  |  |
| ROB pos | 3 | 4 | 6 |  |  |  |  |  |  |  |  |  |  |  |
| state | B | B | B |  |  |  |  |  |  |  |  |  |  |  |

| Reorder Buffer (ROB) |
| --- |
| ROB Entry# | Busy | Op | Status | Destination | Value |
| 1 | yes | PC09 ADD R1,R1,16 | RR | R1 |  |
| 2 | yes | PC10 BL R5,R3,PC04 | RR |  |  |
| 3 | yes | PC04 LD F0,0(R1) | RE | F0 |  |
| 4(tail) | yes | PC05 LD F1,8(R1) | RE | F1 |  |
| 5(head) | yes | PC05 LD F1,8(R1) | EX | - |  |
| 6 | yes | PC06 ADDF F2,F1,F0 | WO | F2 |  |
| 7 | yes | PC07 ST F2,0(R1) | WO | 0(R1) |  |
| 8 | yes | PC08 ADD R3,R3,2 | RR | R3 |  |

-Determining the number of misses at each cache

1024 elements, two elements accessed per iteration, 512 iterations

L3 block is 128 bytes,

PC04 LD    F0,0(R1)

PC05 LD    F1,8(R1)

PC06 ADDF  F2,F1,F0

PC07 ST    F2,0(R1)

Decoupled execution model for bundled (paired) instructions

The state diagram depicts the model for a dynamically scheduled, speculative execution microarchitecture equipped with a Reorder Buffer (ROB) and a set of Reservation Stations (RS). The RSs are allocated during the ISSUE phase, denoted as RAT (Register Alias Allocation Table) in INTEL microarchitectures, as follows: a bundle (2 instructions) if fetched from the QUEUE of decoded instructions and ISSUED if there is a free couple of consecutive entries in the ROB ( head and tail of the ROB queue do not match); a maximum of two instruction are moved into the RS (if available) when all of their operands are available. Access memory instructions are allocated in the ROB and then moved to a load/store buffer (if available) when operands (address and data, if proper) are available .

States are labelled as follows:

WO:	Waiting for Operands (at least one of the operands is not available)

RE:	Ready for Execution (all operands are available)

DI:	Dispatched (posted to a free RS or load/store buffer)

EX:	Execution (moved to a load/store buffer or to a matching and free UF)

WB:	Write Back (result is ready and is returned to the Rob by using in exclusive mode the Common Data Bus CDB)

RR:	Ready to Retire (result available or STORE has completed)

CO:	Commit (result is copied to the final ISA register)

State transitions happen at the following events:

from QUEUE to WO:	ROB entry available, operand missing

from QUEUE to RE:	ROB entry available, all operands available

loop at WO:	waiting for operand(s)

from WO to RE:	all operands available

loop at RE:	waiting for a free RS or load/store buffer

from RE to DI:	RS or load/store buffer available

loop on DI:	waiting for a free UF

from DI to EX:	UF available

loop at EX:	multi-cycle execution in a UF, or waiting for CDB

from EX to WB:	result written to the ROB with exclusive use of CDB

from EX to RR:	STORE completed, branch evaluted

loop at RR:	instruction completed, not at the head of the ROB, or bundled with a not RR instruction

from RR to CO:	bundle of RR instructions at the head of the ROB, no exception raised

Resources
Register-to-Register instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

RS: state DI

UF: EX and WB

Load/Store instructions hold resources as follows:

ROB: from state WO (or RE) up to CO, inclusive;

Load buffer: from state WO (or RE) up to WB

Store buffer: from state WO (or RE) up to EX (do not use WB)

Forwarding: a write on the CDB (WB) makes the operand available to the consumer in the same clock cycle. If the consumer is doing a state transition from QUEUE to WO or RE, that operand is made available; if the consumer is in WO, it goes to RE in the same clock cycle of WB for the producer.

Branches: they compute Next-PC and the branch condition in EX and optionally forward Next-PC to the “in-order” section of the pipeline (Fetch states) in the next clock cycle. They do not enter WB and go to RR instead.

# Text boxes

wo

DI

EX

WB

RR

RE

CO

QUEUE